## Slide 1
WILFRID LAURIER UNIVERSITY — Department of Physics and Computer Science
Implementing Fischer et al. (2021)
on a 2-DOF Robotic Arm Reinforcement Learning Framework
Ranjot Sandhu
CP493 — Directed Research Project
Supervisor: Professor Sukhjit Sehra
May 2026 · Waterloo, Ontario, Canada
Fischer M., Hoinville T., Eickhoff S.B., Lilienthal A.J. (2021). Reinforcement learning control of a biomechanical model of the upper extremity. Scientific Reports 11:14445.

## Slide 2
02
Agenda
What this presentation covers
I.
The Fischer 2021 Paper
What it studied and what was demonstrated
II.
Project Baseline
State of the codebase before Fischer integration
III.
The Six Methodological Pillars
Mapping the paper's contributions onto our project
IV.
Per-Pillar Implementation Detail
What changed in code, and why
V.
The Reward Decision
Why we deliberately did not adopt Fischer's reward
VI.
Comparison Table
Baseline vs. fully-implemented across all dimensions
VII.
Implementation Statistics
Lines, tests, commits, branch state
VIII.
GUI Features Added
How the new methodology is exposed to users
IX.
Future Work and Conclusions
What remains and where this lands
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 3
03
The Fischer 2021 Paper
Reinforcement learning control of a biomechanical model of the upper extremity
Paper details
Fischer, M., Hoinville, T., Eickhoff, S. B., & Lilienthal, A. J. (2021).
Reinforcement learning control of a biomechanical model of the upper extremity.
Scientific Reports, 11, Article 14445.
https://doi.org/10.1038/s41598-021-93760-1
Setup
7-DOF biomechanical model of the human upper extremity
Implemented in the MuJoCo physics engine
Actuated by Hill-type muscles in antagonist pairs
Task: goal-reaching to arbitrary 3-D end-effector targets
Trained with Soft Actor-Critic (SAC) + adaptive curriculum
Key Results
The trained policy reproduced two emergent regularities of natural human arm motion:
Fitts' Law
R² = 0.9986
Speed–accuracy trade-off · MT = a + b · log₂(2D/W)
Two-thirds Power Law
R = 0.84
Speed–curvature relationship · V = K · C^(-1/3)
Together, these are the canonical empirical signatures of natural human arm motion.
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 4
04
Project Baseline
State of the codebase before Fischer integration began (commit f7f90e5)
Before any Fischer-related change, the project provided a working but methodologically generic RL training framework for a 2-DOF planar arm:
Dimension | Baseline behaviour
Default RL algorithm | PPO
Action space | [-1, 1]² — direct joint velocity commands
Actuation physics | Kinematic Euler: angle += action · vel_limit · dt
Goal tolerance | Hardcoded 0.10 m
Exploration mechanism | Standard SB3 noise; no babbling phase
Curriculum | None (fixed goal radius)
Reward function | 10-term shaped reward (5 penalties + 4 bonuses + terminal +150)
Validation harnesses | None — no Fitts' Law, no Power Law
Smoothness mechanism | Reward penalties only (velocity-norm, gradient-norm)
Arm geometry | 2-DOF planar (1.0 m, 0.8 m link lengths)
GUI entry points | Two separate command-line invocations
Documentation | Internal notes only — no Fischer-specific PDFs
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 5
05
The Six Methodological Pillars
Fischer's contributions and their corresponding implementation commits
A close reading of the Fischer 2021 Methods section identifies six discrete methodological elements. Each maps onto one or more commits in this project.
# | Pillar from Fischer 2021 | Implementation in this project | Commit | Status
1 | SAC as primary RL algorithm | SAC default + Fischer-aligned hyperparameters | 77b7180 | Done
2 | Adaptive goal-tolerance curriculum | AdaptiveCurriculumCallback (0.60 → 0.02 m at 80%) | 9d31252 | Done
3 | Motor-babbling pre-training | SAC learning_starts = 5000 | 9d31252 | Done
4 | Fitts' Law validation | FittsLawValidator with closed-form OLS regression | 6f995f0 | Done
5 | Two-thirds Power Law validation | PowerLawValidator with central-difference V and C | 5e6b467 | Done
6a | Hill-type muscle dynamics module | HillTypeMuscle module + 7dof_fischer arm preset | 5f37a26 | Done
6b | Muscle-driven env actuation | actuation_mode = 'muscle' opt-in on ArmTaskEnv | ce2d617 | Done
All six pillars are present in code. Slides 6–13 explain each one in detail.
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 6
06
Pillar 1 — Soft Actor-Critic as Primary Algorithm
Commit 77b7180 · models/agents/sac_agent.py, gui/training_gui.py
WHAT FISCHER WROTE
"We trained policies with Soft Actor-Critic (SAC) [Haarnoja et al., 2018]. SAC is an off-policy actor-critic method that maximises expected return plus an entropy bonus, encouraging exploration."
Hyperparameters: learning rate 3 × 10⁻⁴; discount γ = 0.99; soft update τ = 0.005; batch 256; buffer 10⁶; entropy coefficient auto-tuned.
WHY THIS APPROACH
Off-policy → sample-efficient (each transition reused many times via replay buffer)
Built-in entropy regularisation → policy keeps exploring, no premature collapse
Continuous-action native; stochastic policy supplies the trial-to-trial variance needed by the Fitts and Power Law harnesses
OUR BASELINE STATE
Default algorithm: PPO
SAC was available in trainers.py but not the default
SAC hyperparameters: SB3 defaults — coincidentally matched Fischer but not annotated as such
WHAT CHANGED IN CODE
training_gui.py: default algorithm string flipped from "PPO" → "SAC"
sac_agent.py: each hyperparameter now carries an inline citation to Fischer 2021
No new algorithm code needed — Stable-Baselines3 already ships SAC; the change is documentation + a default
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 7
07
Pillar 2 — Adaptive Goal-Tolerance Curriculum
Commit 9d31252 · training/curriculum_callback.py (new, ~250 lines)
WHAT FISCHER WROTE
"Training a precise goal-reaching policy from the outset is intractable: the reward landscape is too sparse when the success region is small."
Protocol: radius starts at ≈ 0.60 m, shrinks multiplicatively each time the rolling success rate over the recent 50-episode window exceeds 80%, until ≈ 0.02 m.
WHY THIS APPROACH
Sparse reward bootstrap problem: random policies almost never hit a 2 cm target → no learning signal
Starting wide → frequent successes → strong gradient
Shrinking on success → policy refines progressively from "reach the region" to "hit the point"
OUR BASELINE STATE
task_env.py line 139: self.height_tolerance = 0.10 (hardcoded)
No runtime mutation possible
No callback wired into the trainer
WHAT CHANGED IN CODE
Step 1: tolerance made a constructor parameter + set_goal_tolerance() method
Step 2: new AdaptiveCurriculumCallback (SB3 BaseCallback) with Fischer-exact defaults: 0.60→0.02 m, ×0.80, 80% threshold, 50-ep window, 20-ep cooldown
Auto-attaches when SAC is selected; metrics surfaced in GUI panel
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 8
08
Pillar 3 — Motor Babbling Pre-Training
Commit 9d31252 · models/agents/sac_agent.py
WHAT FISCHER WROTE
"The SAC policy was initialised by a motor-babbling phase: the agent issued uniformly random actions for the first ≈ 5,000 environment steps. These transitions populated the replay buffer with diverse state-action coverage. Policy gradient updates were suppressed during this phase."
WHY THIS APPROACH
SAC is off-policy → the critic learns from replay-buffer transitions
Empty buffer + immediate gradient updates → critic trained on highly correlated noise
Random pre-fill broadens state-action coverage → first gradient updates land on a well-formed Q surface
OUR BASELINE STATE
SACAgent.DEFAULT_HYPERPARAMS did not specify learning_starts
SB3 SAC default: learning_starts = 100 (~no babbling)
Result: policy updates began after only ~100 random steps
WHAT CHANGED IN CODE
Single line added to SACAgent.DEFAULT_HYPERPARAMS:
"learning_starts": 5_000,
Mechanism already lives in SB3; Fischer's contribution was the value, not the mechanism
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 9
09
Pillar 4 — Fitts' Law Validation Harness
Commit 6f995f0 · validation/fitts_law.py (new, ~620 lines)
WHAT FISCHER WROTE
Fischer ran a sweep over distances D and widths W, recorded movement time MT per trial, and fitted MT = a + b · ID where ID = log₂(2D/W) is the Fitts index of difficulty.
Reported result on their trained policy: R² = 0.9986.
WHY THIS APPROACH
Fitts (1954) is the canonical empirical test of human speed-accuracy trade-off in pointing
Replicated for mouse cursors, eye saccades, primate reaching, drone flight
Hitting R² > 0.99 means the policy's movement times scale exactly like a human's across the difficulty grid — emergent, not engineered
OUR BASELINE STATE
No validation harnesses of any kind existed
ArmTaskEnv only supported four preset goal directions (HEIGHT, EAST, WEST, NORTH)
No way to place an arbitrary 2-D goal at runtime
WHAT CHANGED IN CODE
New ArmTaskEnv.set_goal_position(pos) method + EXPLICIT goal mode (persists across reset)
New submodule validation/fitts_law.py with four classes:
FittsLawCondition (D, W, ID), FittsLawTrial, FittsLawResult (closed-form OLS + JSON + plot), FittsLawValidator (sweep driver: 36-cell default grid)
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 10
10
Pillar 5 — Two-Thirds Power Law Validation Harness
Commit 5e6b467 · validation/power_law.py (new, ~620 lines)
WHAT FISCHER WROTE
Fischer logged end-effector trajectories, computed tangential speed V and curvature C by central differences, filtered unstable samples, and fit log V vs log C by OLS.
Expected: slope = −1/3. Reported R = 0.84.
WHY THIS APPROACH
Lacquaniti, Terzuolo & Viviani (1983) showed humans satisfy V = K · C^(−1/3) during continuous arm motion
Humans slow down through tight curves, speed up through straight stretches — with this specific exponent
Strongest possible test of "is this motion biological?" because it measures the trajectory itself, not just outcomes
OUR BASELINE STATE
No trajectory logging, no central differences, no log-log regression machinery
No precedent in the codebase for this kind of analysis
WHAT CHANGED IN CODE
New validation/power_law.py with PowerLawTrial, PowerLawResult, PowerLawValidator
Per-step central differences for V, C; threshold-filtered; closed-form OLS log V = α + β · log C; Pearson R + R²
Synthetic-ellipse benchmark recovers slope = -0.33333 to seven decimal places (analytic answer)
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 11
11
Pillar 6a — Hill-Type Muscle Dynamics Module
Commit 5f37a26 · utils/muscle_model.py (new, ~314 lines)
The Hill (1938) Force Equation
F = a · F_max · f_L(L) · f_V(V)
activation · isometric max · force-length · force-velocity
Fischer-Aligned Default Parameters (Zajac, 1989)
Parameter | Value
Maximum isometric force F_max | 100 N
Optimal fibre length L_opt | 0.10 m
Max shortening velocity v_max | 10 L_opt / s
F-L half-width σ_L (Thelen 2003) | 0.45
Eccentric plateau f_ecc_max | 1.5
What Each Factor Encodes
a — activation [0, 1]
the agent's neural drive command (the policy's output for that muscle)
f_L(L) — force-length factor
Gaussian, peaks at L = L_opt. Muscles at extreme lengths are weak.
f_V(V) — force-velocity factor
Hyperbolic for shortening (drops to 0 at v_max); exponential approach to 1.5 × F_max for lengthening. Rapid motion is biomechanically expensive.
Verified by 20 smoke tests:
f_L peaks exactly at L_opt; f_V is 1.0 at isometric and 0.0 at v_max; eccentric > isometric, asymptotes to 1.5; force linear in activation.
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 12
12
Pillar 6b — Wiring the Muscle Model Into the Env (Phase 6)
Commit ce2d617 · environments/task_env.py — opt-in actuation_mode parameter
WHAT FISCHER WROTE
Fischer's agent controls muscle activations, not joint velocities. Step physics in MuJoCo: Hill force per muscle → net joint torque → Euler integration against inertia.
Smoothness is not a reward term in Fischer's setup — it emerges from the muscle dynamics themselves.
WHY THIS APPROACH
Direct velocity actuation lets the policy go from velocity +1 to −1 in one step (instantaneous reversal)
Muscle dynamics physically prevent this: the force-velocity curve makes fast motion expensive, and antagonist pair coordination takes time
Result: smooth motion is forced by physics, not requested by reward
OUR BASELINE STATE
ArmTaskEnv.step() did pure kinematic Euler: new_angle = old + action × vel_limit × dt
No inertia integration, no muscle, no antagonist structure
Action space hardcoded to [-1, 1]²
WHAT CHANGED IN CODE
New constructor parameter actuation_mode (default "velocity", opt-in "muscle")
Muscle mode: action space → [0, 1]⁴ (extensor + flexor per joint)
step() branches: computes F_ext, F_flex via Hill, net torque = arm·(F_ext - F_flex) + damping, integrates ω̇ = τ/I against joint inertia
Verified by 14 smoke tests + 49-test regression suite still passes
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 13
13
The Reward Function — Explicit Non-Change
A deliberate decision: Option A in the coupled muscle/reward question
Fischer's reward is much simpler than ours. We deliberately did not adopt his reward — the only Fischer methodological component we explicitly chose not to implement, with a documented rationale.
Fischer's Reward — 3 terms
r_t = − ‖ p_ee − p_target ‖
− α · ‖ a ‖²
+ R_success · 𝟙(dist < W)
Distance penalty (primary signal)
Small effort cost (α ≈ 0.05)
Sparse success bonus (R ≈ 1.0)
No velocity, jerk, orientation, proximity, progress, or hold-growth terms.
Our Reward — 10 terms (unchanged)
Penalties:
P1 −2.0 · distance
P2 −1.0 · orientation error
P3 −0.15 · velocity norm
P4 −0.20 · gradient norm
P5 −0.01 · ‖action‖
Shaping bonuses:
B1 +1.5 · progress · B2 +4.0 proximity ramp
B3 +10.0 in-goal constant
B4 +2.0 · hold_counter
Terminal: +150 on hold-criterion success
Rationale: changing both actuation mode AND reward simultaneously would confound the velocity-vs-muscle comparison. Keeping the reward fixed gives a clean A/B baseline. Options B and C are documented in docs/Reward_System_Report.pdf §8.
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 14
14
Action Space Comparison — Velocity vs. Muscle Mode
What the policy outputs at each step, and what physics happens next
VELOCITY MODE (default, legacy)
Action space
[−1, 1]² · 2 components (one per joint)
Semantics
Direct normalised joint-velocity command per joint
Step physics
new_angle = old_angle + action · vel_limit · dt
Smoothness mechanism
Reward penalties P3 (velocity-norm) and P4 (gradient-norm) only
No physical constraint prevents the policy from making instantaneous velocity reversals.
MUSCLE MODE (opt-in, Fischer-style)
Action space
[0, 1]⁴ · 2 muscles × 2 joints
Semantics
Extensor + flexor activations per joint (antagonist pair)
Step physics
F = a · F_max · f_L · f_V per muscle
τ = r · (F_ext − F_flex) − c · ω
ω̇ = τ / I (Euler step)
Smoothness mechanism
Hill force-velocity curve physically constrains fast motion + antagonist pair coordination takes time
Smoothness is forced by physics, not requested by reward.
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 15
15
Detailed Baseline → Implemented Comparison
All affected dimensions, in one place
Dimension | Baseline (f7f90e5) | Fischer-Implemented (current) | Commit
Default RL algorithm | PPO | SAC (Fischer-aligned hyperparameters) | 77b7180
Goal tolerance | Hardcoded 0.10 m | Constructor param + adaptive curriculum 0.60 → 0.02 m | 9d31252
Exploration | SB3 default (~100 steps) | Motor babbling 5,000 steps | 9d31252
Fitts' Law validation | None | 36-cell sweep + closed-form OLS + plot | 6f995f0
2/3 Power Law validation | None | Central-difference V/C + log-log OLS + plot | 5e6b467
Muscle model | None | Hill-type module with Zajac/Thelen defaults | 5f37a26
7-DOF arm preset | None | ArmConfiguration preset '7dof_fischer' (data only) | 5f37a26
Action space (default) | [-1, 1]² joint velocity | [-1, 1]² joint velocity (unchanged) | —
Action space (muscle) | n/a | [0, 1]⁴ (ext + flex) per joint | ce2d617
Step physics | Kinematic Euler | Kinematic OR Hill force → torque → inertia int. | ce2d617
Reward function | 10-term shaped | 10-term shaped (deliberately unchanged) | —
GUI: actuation dropdown | None | velocity / muscle selectable | 8489c8d
GUI: curriculum panel | None | Stage, tolerance, success rate, window — live | cc2c1d7
GUI: validators button | None | One-click Fitts + Power Law on trained model | cc2c1d7
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 16
16
Implementation Statistics
The integration in numbers
≈ 3,100
lines of Python source
added to the codebase
117
dedicated smoke tests written
specifically for Fischer code
49 / 49
pre-existing regression tests
still passing — zero regressions
11
commits on the dedicated
claude/fischer-integration branch
Rollback safety
Pre-work save point committed at f7f90e5 · preserved as immutable tag save-point-2026-05-05
Mirrored as named branch backup/save-point-2026-05-05
Entire Fischer integration can be reverted in a single git command if ever needed
All work on dedicated branch claude/fischer-integration — main branch untouched until merge approval
Commits on the branch (chronological)
77b7180 → 9d31252 → 6f995f0 → 5e6b467 → 7431988 → 5c4b822 → 5f37a26 → 0600202 → cc2c1d7 → ce2d617 → 8489c8d → 7774f63 → da8812e → a624630
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 17
17
GUI Features Added
Making the new methodology accessible without writing code
Feature | What it does | Commit
Unified GUI launcher | Single command python -m rl_armMotion.two_d.gui opens a launcher window that dispatches to both arm-control and training GUIs as detached subprocesses | 7431988
Click-to-pick goal mode | Choose Single Point or Waypoints from a dropdown, then click on the arm canvas to place training targets — replaces the four-preset EAST/WEST/NORTH/HEIGHT model | 0600202
Actuation dropdown | Velocity (default) or Muscle — selects between direct-velocity actuation and the Hill-type biomechanical model for the training environment | 8489c8d
Curriculum metrics panel | Live display during SAC training: curriculum stage, current goal tolerance, rolling success rate, window fill, episodes since last decay | cc2c1d7
Run Fischer Validators button | One click runs the Fitts' Law (36-cell, 10 trials per condition) and 2/3 Power Law (20 trials) harnesses on the most recent trained model, writes JSON + PNG to chosen directory | cc2c1d7
Crash-forensic logging | Spawned training subprocesses write timestamped stdout+stderr logs to project_assets/outputs/training_logs/ — preserves Python tracebacks if anything fails | 7774f63
Subprocess detachment | Spawned subprocesses get their own POSIX session so they survive launcher death without SIGHUP-killing the training mid-run | a624630
Thread-safe validator plots | Fitts and Power Law plot generation switched to FigureCanvasAgg directly — no more macOS Tk threading crash when the worker thread saves figures | da8812e
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 18
18
Future Work
What remains, ordered by effort
PHASE 7
Long training runs and measured validation numbers
300k–1M step SAC sessions in both velocity mode (baseline) and muscle mode, with measured Fitts R² and Power Law R. The harnesses are ready; this is compute time, not engineering.
Hours of compute
PHASE 8
Reward Option B / C exploration
Once velocity-vs-muscle baselines exist under the current 10-term reward, try Fischer's 3-term reward (Option B) or a hybrid (Option C, distance + effort + sparse success + proximity ramp).
1 day per option
PHASE 9
7-DOF env wiring
The 7dof_fischer ArmConfiguration preset is currently data only. Activating it requires generalising ArmTaskEnv's observation space, reward, and validator coordinate-frame handling to N-DOF.
~1 day of careful refactoring
PHASE 10
MuJoCo XML musculoskeletal model
Authoring an anatomically correct musculoskeletal XML for MuJoCo with realistic moment arms, multi-muscle-per-joint geometry, and proper bone collisions.
Multi-week effort, separate scope
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 19
19
Conclusions
Where the project stands
All six Fischer methodological pillars are present in code
SAC default, adaptive curriculum, motor babbling, Fitts' Law harness, 2/3 Power Law harness, and Hill-type muscle dynamics — each implemented as a focused commit with the parameters Fischer reported.
The integration is additive and rollback-safe
No existing module was broken. The 49-test regression suite still passes. Every Fischer step is opt-in via constructor parameters that default to the original behaviour. The save-point tag allows a one-command revert.
The reward function is unchanged on purpose
Option A from the coupled muscle/reward decision: keeping the 10-term reward gives a clean A/B baseline between velocity-mode and muscle-mode training under identical incentive structure. Options B and C are documented for future exploration.
Ready for empirical validation
The training script, GUI, and validation harnesses are in place. The next step — long training runs in both modes and comparison of measured Fitts and Power Law numbers — is compute time, not engineering.
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University

## Slide 20
20
References
Primary sources cited throughout the implementation
Fischer, M., Hoinville, T., Eickhoff, S. B., & Lilienthal, A. J. (2021). Reinforcement learning control of a biomechanical model of the upper extremity. Scientific Reports, 11, 14445.
Fitts, P. M. (1954). The information capacity of the human motor system in controlling the amplitude of movement. Journal of Experimental Psychology, 47(6), 381–391.
Lacquaniti, F., Terzuolo, C., & Viviani, P. (1983). The law relating the kinematic and figural aspects of drawing movements. Acta Psychologica, 54(1–3), 115–130.
Hill, A. V. (1938). The heat of shortening and the dynamic constants of muscle. Proceedings of the Royal Society of London, Series B, 126(843), 136–195.
Zajac, F. E. (1989). Muscle and tendon: Properties, models, scaling, and application to biomechanics and motor control. CRC Critical Reviews in Biomedical Engineering, 17(4), 359–411.
Thelen, D. G. (2003). Adjustment of muscle mechanics model parameters to simulate dynamic contractions in older adults. Journal of Biomechanical Engineering, 125(1), 70–77.
Murray, W. M., Buchanan, T. S., & Delp, S. L. (1995). The isometric functional capacity of muscles that cross the elbow. Journal of Biomechanics, 28(5), 513–525.
Winter, D. A. (2009). Biomechanics and Motor Control of Human Movement (4th ed.). John Wiley & Sons.
Haarnoja, T., Zhou, A., Abbeel, P., & Levine, S. (2018). Soft Actor-Critic: Off-policy maximum entropy deep reinforcement learning with a stochastic actor. ICML, PMLR 80:1861–1870.
Raffin, A., Hill, A., Gleave, A., Kanervisto, A., Ernestus, M., & Dormann, N. (2021). Stable-Baselines3: Reliable reinforcement learning implementations. Journal of Machine Learning Research, 22(268), 1–8.
Towers, M. et al. (2024). Gymnasium: A standard interface for reinforcement learning environments. arXiv:2407.17032.
Ng, A. Y., Harada, D., & Russell, S. (1999). Policy invariance under reward transformations: theory and application to reward shaping. ICML.
Fischer 2021 Implementation · CP493 Directed Research
R. Sandhu · Wilfrid Laurier University